## Slide 1: Part I Syllabus – Fundamental Underlying Layers
Week​ | Date​ | Subject​
Week 1 | 9/Jan/2023​ | Introduction: Course Logistics and Internet History​
 | 11/Jan/2023​ | Layered Network Architecture​
Week 2 | 16/Jan/2023​ | Physical-layer Resilience
 | 18/Jan/2023​ | Data Link Layer: Flow Control​
Week 3 | 25/Jan/2023​ (no class on 23/Jan/2023, a holiday​) | Data Link Layer: Error Control​
Week 4 | 30/Jan/2023​ | Local Area Network: Introduction​
 | 01/Feb/2023​ | Local Area Network: Medium Access Control (MAC)​
Week 5 | 06/Feb/2023​ | Local Area Network: Ethernet​
 | 08/Feb/2023​ | Local Area Network: Ethernet Evolutions​
Week 6 | 13/Feb/2023​ | Wireless Local Area Network (WLAN): Overview and 802.11
 | 15/Feb/2023​ | First Part: WLAN’s Multi-Access Reservation Protocol (MARP); Second Part: A Brief Overview of Network Paradigms​
Week 7 | 20/Feb/2023 | Network Paradigms​: Circuit Switching versus Packet Switching
 | 22/Feb/2023 | Mobile Access Networks

## Slide 2: Additional Materials
The related content talked today in https://eclass.teicrete.gr/modules/document/file.php/TP326/%CE%98%CE%B5%CF%89%CF%81%CE%AF%CE%B1%20(Lectures)/Computer_Networking_A_Top-Down_Approach.pdf is as follow:
  WiFi: 802.11 Wireless LANs: Page 526 – Page 546
  Cellular Internet Access: Page 547 – Page 555
  Mobility Management: Principles: Page 555 – Page 564
You can also find other video materials about
  802.11 WiFI https://www.youtube.com/watch?v=t3FVP5wuG4g
  Wireless Communication https://www.youtube.com/watch?v=8T7orRAQgic&list=PLCyR4nKNLRkFTER9ohRBnbRFK0pWe0Qtf&index=1&t=61s

## Slide 3: Mobile Access

## Slide 4: SC2008/CZ3006/CE3005 ​ Computer Network
Lecture 9
Mobile Access Networks:
From 1G to 5G
(Not Examinable)

## Slide 5: Contents
Wireless Link Standards
  802.11 (Wi-Fi)
  Cellular (1G to 5G)
  802.15 (e.g., ZigBee)
  802.16 (WiMax)
Cellular Networks
  Network architecture
  MAC protocols
  1G to 5G
Mobility handling
  Mobility vocabulary
  Indirect routing
  Direct routing

## Slide 6: Wireless Link Standards

## Slide 7: Characteristics of Selected Wireless Link Standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data

## Slide 8: Characteristics of Selected Wireless Link Standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data

## Slide 9: Characteristics of Selected Wireless Link Standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data

## Slide 10: Characteristics of Selected Wireless Link Standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data
Zigbee

## Slide 11: Characteristics of Selected Wireless Link Standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data

## Slide 12: Cellular Networks: 1G to 5G

## Slide 13: Boost of Mobiles

## Slide 14: Cellular Network Architecture
Mobile
Switching
Center
Public telephone
network, and
Internet
Mobile
Switching
Center
connects cells to wide area net
manages call setup
handles mobility
MSC
covers geographical region
base station (BS) similar to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 15: Interconnection of Cellular Networks
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers

## Slide 16: Cellular Network: The First Hop
Two techniques for sharing mobile-to-BS radio spectrum
  Combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
  CDMA: code division multiple access
frequency
bands
time slots

## Slide 17: Handover and Roaming
  Handover: transfer a call or data session from one cell to another within the same cellular network
    Handled by Mobile Switching Center (MSC), no charge
  Roaming: the mobile moves from its home cellular network to a foreign network
Handover
Roaming

## Slide 18: Cellular Standards: Brief Survey
1G: analog, 3 decades ago
2G/2.5G: 50-384kbps, 2 decades ago
3G: up to 14Mbps
4G: up to 300Mbps
Last decade
5G: up to 430Mbps using sub-6GHz
up to 10Gbps using >24GHz
From 2019

## Slide 19: Cellular Standards: Brief Survey
2G systems: voice channels
  IS-136 TMDA: combined FDMA/TDMA (North America)
  GSM (global system for mobile communications): combined FDMA/TDMA
    Most widely deployed
  IS-95 CDMA: code division multiple access
IS-136
GSM
IS-95
GPRS
EDGE
CDMA-2000
UMTS
TDMA/FDMA
Don’t drown in a bowl of alphabet soup: use this for reference only

## Slide 20: Cellular Standards: Brief Survey
2.5G systems: voice and data channels
  2G extensions: for those who can’t wait for 3G
  General packet radio service (GPRS)
    Evolved from GSM
    Data sent on multiple channels (if available)
  Enhanced data rates for global evolution (EDGE)
    Also evolved from GSM, using enhanced modulation
    Data rates up to 384kbps
  CDMA-2000 (phase 1)
    Data rates up to 144kbps
    Evolved from IS-95

## Slide 21: 2G (voice) Network Architecture
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
MSC
Public switched
telephone
network
Gateway
MSC
G

## Slide 22: 2.5G (Voice+Data) Network Architecture
BSC
MSC
SGSN
Public switched
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
with existing cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 23: Cellular Standards: Brief Survey
3G systems: voice + data
  Universal Mobile Telecommunications Service (UMTS)
  CDMA in TDMA slots
  Data service: up to 14 Mbps
4G systems: data
  All-IP network: voice in data packets
  New wireless access technologies: OFDM, MIMO, etc
  Data rate: up to 300 Mbps

## Slide 24: Cellular Standards: Brief Survey
5G systems: massive data
  Microwaves (4G) + millimeter waves (high bandwidth)

## Slide 25: Mobility (Roaming) Handling

## Slide 26: What Is Mobility?
Spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same point of access
mobile user, passing through multiple points of access while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 27: Mobility: Vocabulary
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
Permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote
wide area network
correspondent

## Slide 28: Mobility: Vocabulary
Care-of-address: address in visited network.
(e.g., 79,129.13.2)
wide area network
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
Permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 29: Mobility: Approaches
Let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange
  Routing tables indicate where each mobile located
  No changes to end-systems
Let end-systems handle it:
  Indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  Direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 30: Mobility: Approaches
Let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange
  Routing tables indicate where each mobile located
  No changes to end-systems
Let end-systems handle it:
  Indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  Direct routing: correspondent gets foreign address of mobile, sends directly to mobile
not
scalable
to millions of
mobiles

## Slide 31: Mobility: Registration
End result:
  Foreign agent knows about mobile
  Home agent knows location of mobile
wide area network
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent: “this mobile is resident in my network”

## Slide 32: Mobility via Indirect Routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 33: Indirect Routing: Comments
Mobile uses two addresses
  Permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  Care-of-address (Foreign address): used by home agent to forward datagrams to mobile
Triangle routing: correspondent-home network-mobile
  Inefficient when correspondent & mobile are in same network

## Slide 34: Indirect Routing: Moving Between Networks
Suppose mobile user moves to another network
  Register with new foreign agent
  New foreign agent registers with home agent
  Home agent update care-of-address for mobile
  Packets continue to be forwarded to mobile (but with new care-of-address)
Mobility, changing foreign networks
  Transparent: ongoing connections can be maintained!

## Slide 35: Mobility via Direct Routing
wide area network
home
network
visited
network
4
2
4
1
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent
3

## Slide 36: Mobility via Direct Routing: Comments
Overcome triangle routing problem
Non-transparent to correspondent: correspondent must get care-of-address from home agent
  What if mobile changes visited network?

## Slide 37: Accommodating Mobility with Direct Routing
  Anchor foreign agent: FA in first visited network
  Data always routed first to anchor FA
  When mobile moves: new FA arranges to have data forwarded from old FA (chaining)
wide area network
1
foreign net visited
at session start
anchor
foreign
agent
2
4
new foreign
agent
3
5
correspondent
agent
correspondent
new
foreign
network

## Slide 38: Handling Mobility in Cellular Networks
Home network: network of cellular provider you subscribe to (e.g., SingTel, M1)
  Home location register (HLR): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
Visited network: network in which mobile currently resides
  Visitor location register (VLR): database with entry for each user currently in network
  Could be home network

## Slide 39: GSM: Indirect Routing to Mobile
Public switched
telephone
network
mobile
user
home
Mobile
Switching
Center
HLR
home
network
visited
network
correspondent
Mobile
Switching
Center
VLR
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile

## Slide 40: Wireless, Mobility: Impact on Higher Layer Protocols
Logically, impact should be minimal …
  Best effort service model remains unchanged
  Higher layers can (and do) run over wireless, mobile
… but performance-wise
  Packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  Delay impairments for real-time traffic
  Limited bandwidth of wireless links

## Slide 41: Learning Objectives
Wireless Link Standards
  Read the characteristics of the standards
Cellular Networks
  Understand the network architecture
  Understand the key features of 1G to 5G
Mobility (roaming) handling
  Read mobility vocabulary
  Understand indirect and direct routing