## Slide 1: Part I Syllabus – Fundamental Underlying Layers
Week​ | Date​ | Subject​
Week 1 | 9/Jan/2023​ | Introduction: Course Logistics and Internet History​
 | 11/Jan/2023​ | Layered Network Architecture​
Week 2 | 16/Jan/2023​ | Physical-layer Resilience
 | 18/Jan/2023​ | Data Link Layer: Flow Control​
Week 3 | 25/Jan/2023​ (no class on 23/Jan/2023, a holiday​) | Data Link Layer: Error Control​
Week 4 | 30/Jan/2023​ | Local Area Network: Introduction​
 | 01/Feb/2023​ | Local Area Network: Medium Access Control (MAC)​
Week 5 | 06/Feb/2023​ | Local Area Network: Ethernet​
 | 08/Feb/2023​ | Local Area Network: Ethernet Evolutions​
Week 6 | 13/Feb/2023​ | Wireless Local Area Network (WLAN): Overview and 802.11
 | 15/Feb/2023​ | First Part: WLAN’s Multi-Access Reservation Protocol (MARP); Second Part: A Brief Overview of Network Paradigms​
Week 7 | 20/Feb/2023 | Network Paradigms​: Circuit Switching versus Packet Switching
 | 22/Feb/2023 | Mobile Access Networks

## Slide 2: Additional Materials
The related content about flow control talked today in https://eclass.teicrete.gr/modules/document/file.php/TP326/%CE%98%CE%B5%CF%89%CF%81%CE%AF%CE%B1%20(Lectures)/Computer_Networking_A_Top-Down_Approach.pdf is as follow:
  stop-and-wait: Page 207- Page 218
  sliding window: Page 218- Page 229
And here is another resource for your reference https://www.geeksforgeeks.org/flow-control-in-data-link-layer/
You can also find other video materials about
  stop-and-wait Stop-and-Wait Protocol - YouTube
  sliding window Sliding Window Protocol - YouTube

## Slide 3: Drinking from Fire Hose

## Slide 4: SC2008/CZ3006/CE3005
Lecture 3
Data Link Layer (DLL): Flow Control

## Slide 5: Contents
Data Link Layer Fundamentals
  DLL Services
  Framing mechanisms
  Link configuration
Flow Control in DLL
  Main purpose of flow control
  Stop-and-wait mechanism
  Sliding window mechanism
Encapsulation:
information gets bulkier and bulkier

## Slide 6: Data Link Layer Fundamentals

## Slide 7: Data Link Layer (DLL): Roles
DLL Services
  Framing: encapsulate each network-layer datagram within a link-layer frame before transmission over the link
  Link Access: MAC protocol specifying the rules by which a frame is transmitted onto the link
  Flow Control: control of data flow to ensure sender not overwhelm the receiver with data
  Reliable Delivery: move each network-layer datagram across the link without error
Not Examinable

## Slide 8: Framing
Byte Oriented (Character Oriented):
  Information is framed into a fixed 8-bit basic unit.
  Some of these basic units are used for signaling (protocol control).
  Good solution when digital technology was in its primitive age (late 60s).
Bit Oriented (HDLC)
  A flag is used to frame the bits sent.
  Header/Trailer are used to describe the content of a frame. Frames may be used for control.
  Used by all modern protocols (e.g., HDLC, PPP, Ethernet, etc).
Not Examinable

## Slide 9: Byte-Oriented Async. Transmission
Pre-determined frame format
  Start/stop bit
  Parity check bit
  Data bits
idle state
of line
start bit
1
0
5 to 8 data bits
odd or even parity bit, if used
stop bit(s) 1 or 2
unpredictable time interval between characters
start bit
. . .
Not Examinable

## Slide 10: Link Configuration/Access
Objective: determine who gets to transmit at when on a link
Topology: physical arrangement of stations
  Point-to-Point: pairs of hosts are directly connected
  Broadcast: all stations share a single channel
Duplexity
  Half Duplex: Only one party may transmit at a time.
  Full Duplex: Allows simultaneous transmission and reception between two parties (e.g., two logical half-duplex channels on a single physical channel).
Not Examinable

## Slide 11: Topology
Point-to-point:
Point-to-Multipoint (Broadcast):
T1
T2
T3
T4
All terminals share the same medium controlled by the primary station (mainframe)
Not Examinable

## Slide 12: Flow Control
All slides about Flow Control are Examinable.

## Slide 13: Functions and Mechanisms
Flow control
  Ensuring that a transmitting station does not overwhelm a receiving station with data, i.e., buffers at the receiver do not get overflowed.
  No frame error
Two Flow-Control Mechanisms
  Stop-and-Wait
  Sliding Window
A
B
Examinable

## Slide 14: Stop-and-Wait Flow Control
A
B
Operations:
 A packs binary information into a frame
 A sends the frame to B
 A waits for an ACK
 When B has received the frame, B sends an ACK
 When A has received the ACK, A repeats 
frame
ACK


Examinable

## Slide 15: Frame Flow in Stop-and-Wait
sender
receiver
time
f0
ACK1
f0
f0
f1
f1
ACK0
f1
f0
ACK1
f0
f0
ACK1 means the receiver expects f1, implying f0 is received successfully
…
Binary sequence number is sufficient
Examinable

## Slide 16: Flow-Control Link Utilization
sender
receiver
time
Tframe
Tcycle
Tproc
Tcycle: Total time needed to send a frame
Tproc: Processing time
Tframe: Frame transmission time (i.e., to pump out a frame’s bits from your computer)
Tack: ACK transmission time
Tprop: Signal Propagation delay
Tcycle = Tframe + Tprop + Tproc + Tack + Tprop + Tproc
Tproc
U
(Link Utilization)
=
the time that the link
carries useful information
the total time
Tframe
Tcycle
=
Examinable

## Slide 17: Link Utilization for Stop-and-Wait
Assumptions
  Input is saturated
  No error
  Ignoring Tack & Tproc
We get:
Tcycle = Tframe + 2 Tprop
Then:
U = Tframe / (Tframe + 2 Tprop)
= 1 / (1+2a)
where:
we define a = Tprop / Tframe
Parameter ‘a’ is called Normalized Propagation Delay
Examinable

## Slide 18: Example
A communication link exists between two nodes A and B. The transmission rate on the link is 2.4 Mbps. The distance between A and B is 50 km and the signal velocity is 2x108 m/s. The frame length is 300 bytes. No frame error. Calculate the link unitization for the stop-&-wait flow control mechanism.
A
B
R= 2.4 Mbps, L=300 bytes =2400bits
D=50km, v = 2x108 m/s
U=1/(1+2a)
a = Tp/Tf
Tp=D/V=5x104/2x108 = 250 μs
Tf=L/R=2400/2.4x106 = 1000 μs
a = 0.25
U=1/(1+2*0.25)
= 2/3
Here Tp and Tf are short for
Tprop and Tframe, respectively.
μs means microsecond; i.e., 10-6 seconds.
Examinable

## Slide 19: Stop-and-Wait: Disadvantages
If frame or ACK is lost, long waiting time is expected
  To fix this, use a TIMEOUT control in the sender
If the normalized propagation delay is long, the sender must wait a long time before it can perform the next transmission.
  The link utilization is low.
  To fix this, use Buffers at the sender/receiver (sliding window operation). This will improve the numerator. Note that the denominator 1+2a cannot be improved.
Examinable

## Slide 20: Sliding Window Flow Control
Allows multiple frames to be in transit.
Sender and Receiver have buffer N long.
Sender can send up to N frames without receiving ACKs.
Each frame is numbered.
ACK includes number of next expected frame.
Sequence number bounded by field size (k bits)
  Frames are numbered modulo 2k
  Sequence number [0, 2k-1]
Examinable

## Slide 21: Sliding Window Operations
Sender
  Move lower bound when frames sent
  Move upper bound when acks received
Receiver
  Move lower bound when frames received
  Move upper bound when acks sent
Examinable

## Slide 22: Sliding Window Operations
Sender maintains a window, containing frame numbers that can be transmitted.
Sender window shrinks from trailing edge (left side) as frames are sent.
Receiver maintains a window as well, its window shrinks from trailing edge as frames are received.
Receiver’s window expands from the leading edge (right side) as ACKs are sent.
Sender’s window expands from the leading edge as ACKs are received.
Examinable

## Slide 23: Sliding Window: Example
Examinable

## Slide 24
Sliding Window Algorithm
Not Examinable

## Slide 25: Window Size Consideration
Say, window size, N = 3
with k=1 bit sequence number
0 1 0
receiver
sender
ack1
0 1 0 1 0 1 0 1
Sender: Do you ask for a retransmission of the transmitted frame or a new frame?
 Is the second 0 a new frame or the retransmitted frame?
 Which frame is to be transmitted next after receiving ack1?
Receiver: Is it a retransmission or a new frame?
Examinable

## Slide 26
N ≤ 2k
Based on the previous slide, for window size N and k bits sequence number, we need
Examinable

## Slide 27: Sliding Window: Other Features
Receiver can acknowledge frames without permitting further transmission (by sending ‘Receive Not Ready’, RNR frame). Receiver must send a normal acknowledgement to resume.
ACK can be piggybacked on the data frames in the reverse direction.
sender
receiver
F0
F1
RNR2
sender
receiver
F0
F1
F0+ACK2
Examinable

## Slide 28: Sliding Window: Performance
Performance depends upon
  Parameter a, and
  Window size, N.
Assumption: Tack and Tproc are negligible.
Frame transmission time = 1 (normalized to itself)
Normalized propagation delay (one-way) = a
We need to consider two cases:
  N  2a +1: Station can transmit continuously without exhausting its window  U = 1.0
  N < 2a +1: Station’s window is exhausted at t = N, and the station cannot send additional frames until t = 2a + 1,  U = N/(1 + 2a)
(assume error-free operation):
Examinable

## Slide 29: Case I: N  2a +1 [U=1]
t = 2
A
B
t = 1
A
B
t = 0
A
B
Frame 1
Frame 2
Frame 1
t = a
A
B
Frame a
Frame a-1
Frame 2
Frame 1
. . .
t = a+1
A
B
Frame 3
Frame 2
Frame a+1
Frame a
A
. . .
t = 2a+1
A
B
Frame a+3
Frame a+2
Frame 2a+1
Frame 2a
A
. . .
Examinable

## Slide 30: Case II: N  2a +1 [U=N/(1+2a) ]
t = 1
A
B
t = 0
A
B
Frame 1
t = a
A
B
Frame a
Frame a-1
Frame 2
Frame 1
. . .
t = a+1
A
B
Frame 3
Frame 2
Frame a+1
Frame a
A
. . .
t = N
A
B
Frame N-a+2
Frame N
Frame N-1
A
Frame N-a+1
. . .
. . .
t = 2a+1
A
B
Frame a+2
Frame N
A
no tx (ie. wastage)
Examinable

## Slide 31: Sliding Window: Performance
sender
receiver
0 1
0 1
time
Tuseful
Tcycle
0 1
2 3
2 3
ACK1
2 3
0 1
Window Size = N
Tuseful = N*Tframe
Tcycle = Tframe+2*Tprop
ACK2
ACK3
ACK0
Examinable

## Slide 32: Flow Control: Link Utilization
N=1
N=7
N=127
Link Utilization versus a
Stop-and-Wait
Examinable

## Slide 33: Learning Objectives
Data Link Layer Fundamentals
  To understand its (four) main functions
Flow Control
  To understand its main purpose
  Stop-and-Wait Flow-Control Mechanism
    Operational protocol
    Link utilization calculation
  Sliding Window Flow-Control Mechanism
    Operational protocol
    Window size determination
    Link utilization calculation (two cases)