## Slide 1: Part I Syllabus – Fundamental Underlying Layers
Date​ | Subject​ | File​
Week 1:​ 9/Jan/2023​ 11/Jan/2023​ | Introduction: course logistics and Internet history​ | M1-L1-Introduction.pptx​
 | Layered Network Architecture​ | First part of M1-L2-Network Layer & Physical Resilience.pptx​
Week 2:​ 16/Jan/2023​ 18/Jan/2023​ | Physical Layer: Network Resilience​ | Second part of M1-L2-Network Layer & Physical Resilience.pptx​
 | Data link layer – Flow control​ | M1-L3-DLL-Flow Control.pptx​
Week 3:​​ 25/Jan/2023​ | Data link layer – Error control​ | M1-L4-DLL-Error Control.pptx​
Week 4:​ 30/Jan/2023​ 01/Feb/2023​ | Local area network – Introduction​ | M1-L5-LAN-Introduction.pptx​
 | Local area network – MAC​ | M1-L6-LAN-MAC.pptx​
Week 5:​ 06/Feb/2023​ 08/Feb/2023​ | Local area network – Ethernet​ | First part of M1-L7-LAN-Ethernet.pptx​
 | Local area network – Ethernet Evolutions​ | Second part of M1-L7-LAN-Ethernet.pptx​
Week 6:​ 13/Feb/2023​ 15/Feb/2023​ | Local area network – WLAN​ | M1-L8-LAN-WLAN.pptx​
 | Mobile Access Networks | M1-L9-Mobile.pptx
Week 7: 20/Feb/2023 22/Feb/2023 | E-learning for Network paradigms | M1-L10-Paradigms.pptx
 | Reviewing all contents taught in previous lectures | 

## Slide 2: Additional Materials
The related content talked today in https://eclass.teicrete.gr/modules/document/file.php/TP326/%CE%98%CE%B5%CF%89%CF%81%CE%AF%CE%B1%20(Lectures)/Computer_Networking_A_Top-Down_Approach.pdf is as follow:
  Error detection: Page 438 – Page 445
  Automatic Repeat Request (ARQ): Page 207 – Page 230
You can also find other video materials about
  Error detection https://www.youtube.com/watch?v=EMrY-8m8D1E
  Stop-and-Wait ARQ https://www.youtube.com/watch?v=YdkksvhkQGQ
  Go-Back-N ARQ https://www.youtube.com/watch?v=QD3oCelHJ20
  Selective Reject ARQ https://www.youtube.com/watch?v=WfIhQ3o2xow

## Slide 3: Chat over Unreliable Network
Do you want to go out for a movie tonight?
Sure
Shoot!
Wrong message!
Sure
Sure
Call
Contact lnfo

## Slide 4
Lecture 4
Data Link Layer (DLL): Error Control

## Slide 5: Contents
Error Detection
  Parity Check
  CRC
Automatic Repeat ReQuest (ARQ)
  Stop-and-Wait ARQ
  Go-Back-N ARQ
  Selective Reject ARQ

## Slide 6: Error Control in Data Link Layer
Objective
  To detect and correct errors that occur in frame transmission
Frame Error in Data Link Layer (DLL)
  Lost Frame: the receiver does not receive a frame (or the header was corrupted such that the frame was not recognizable)
  Damaged Frame: the receiver receives a frame, but some of its bits are in error

## Slide 7: Error Detection Techniques

## Slide 8: Error Detection: Parity Check
Parity Check (Odd/Even Parity): A single bit is appended to the original message (usually 7-bit) to describe the message characteristics.
1 0 0 1 1 0 1
?
7 bits
8 bits
Parity bit
Message
Even Parity: The total number of 1s is even, ie. 10011010
Odd Parity: The total number of 1s is odd, ie. 10011011
 However, Parity Check can only detect odd numbers of errors！
Not Examinable

## Slide 9: 7 Prisoners with 1 Psycho Cop
You are in a group of 7 prisoners who are captured by a crooked, psycho cop. He decides to execute the lot of you, but to play a game to give some of you a chance to live. His plan is to put either a blue or red hat on each of your heads, and then he will ask each person what color his hat is. If they guess correctly, they may leave freely. Otherwise, BANG! he shoots them dead.
The cop will first line all of you up in a single line, all facing in one direction, such that each person is facing the next prisoner's back. Every criminal can see the hats of every one in front of them, but not their own hat or anyone behind them. The Cop will ask each of you in order, starting from the back of the line and moving forward.
https://jonc101.tripod.com/brainteaser/key/04-03-prisonerLine.htm
Not Examinable

## Slide 10: Error Detection: CRC
Cyclic Redundancy Check (CRC): multiple parity bits are appended to the original message.
message (M bits)
CRC(g)
message (M bits)
CRC
M + k bits
CRC(g)
received info (M+k bits)
tx
Remainder
(Remainder = 0 indicates no error)
sender
receiver
Not Examinable

## Slide 11: Error Correction Technique: Automatic Repeat Request (ARQ)
All slides about Automatic Repeat Request (ARQ) are examinable.

## Slide 12: Error Correction Techniques
Forward Error Correction (FEC)
  Send more redundant bits in the message
  Example: Hamming code, Reed-Solomon code
Automatic Repeat Request (ARQ)
  Retransmission after timeout: The source retransmits a frame when an expected ACK fails to return within a predetermined time duration
  Retransmission when requested: The destination replies a negative ACK to inform the source about an error. The source then retransmits the corrupted frames accordingly.

## Slide 13: ARQ Variants
Commonly implemented ARQ mechanisms:
  Stop-and-Wait ARQ
  Sliding Window - Go-back-N ARQ:
    Frames are accepted strictly in the sequence.
  Sliding Window - Selective-Reject ARQ:
    Sometimes called “Selective Repeat ARQ”. Frames which arrive out of sequence (but are within the open window at the receiver) are accepted.
Flow Control
Stop-and-Wait
Sliding Window
Go-back-N
Selective Reject
Stop-and-Wait
Examinable

## Slide 14: Stop-and-Wait ARQ: Illustration
(duplicate frame, to discard)
timeout
retransmission
F
0
F
0
ACK
1
F
0
ACK
1
timeout
retransmission
F
1
…
ACK
0
receiver
sender
time
lost
(loss of frame)
(loss of ACK)
Examinable

## Slide 15: Stop-and-Wait ARQ (Protocol)
Source: transmits a single frame and waits for ACK.
Destination:
    Frame received correctly - send an ACK.
    Damaged frame received - There are two variations:
      Discard it, and do nothing else.
      Send a NAK (negative acknowledgement).
Source:
    If ACK is received properly, transmit next frame.
    If NAK is received, retransmit the same frame.
    If no ACK is received within timeout, transmitter timeouts, and retransmits the same frame.
    If ACK is damaged, transmitter will not recognize it, transmitter will timeout and retransmit the same frame. Receiver gets two copies of the same frame, discard one.
Examinable

## Slide 16: Stop-and-Wait ARQ: Performance
Link Utilization
=
The time that the link
carries useful information
The total time
Tpropagation
Tframe
a =
P: Frame loss probability
a: normalized propagation delay
Examinable

## Slide 17: Example
A communication link exists between two nodes A and B. The transmission rate on the link is 2.4 Mbps. The distance between A and B is 50 km and the signal velocity is 2x108 m/s. The frame length is 300 bytes. Frame loss probability is 0.1. Calculate the link unitization for the stop-&-wait ARQ mechanism.
R= 2.4 Mbps, L=300 bytes =2400bits
H=50km, V = 2x108 m/s
P=0.1
U=(1-P)/(1+2a)
a = Tp/Tf
Tp=H/V=5x104/2x108 = 250 μs
Tf=L/R=2400/2.4x106 = 1000 μs
a = 0.25
U=(1-0.1)/(1+2*0.25)
= 0.6
A
B
Examinable

## Slide 18: Go-Back-N ARQ: Illustration
The sender must
go back to
transmission
F
1
when NAK
1
is
received
The r
eceiver
expects
F
1
, but
F
2
arrives
instead. Hence
NAK1 is replied.
All received
frames will be
discarded
until
F
1
arrives.
receiver
sender
F
2
F
0
F
1
ACK
1
NA
K
1
F
3
F
2
F
1
AC
K
2
F
3
AC
K
3
AC
K
4
time
(discarded)
(discarded)
Cautious Scheme !
Examinable

## Slide 19: Go-Back-N ARQ: Protocol
Source: transmits frames sequentially based on sliding window.
Destination:
  For error-free frames, ACKs are sent as usual. ACK is usually called ‘Receive Ready’ (RR)
  Can use ‘Receiver Not Ready’ (RNR) for controlling the flow.
  If a damaged frame is received, NAK is sent. NAK is usually called ‘Reject’ (REJ). The destination discards that frame, and all subsequent frames until erroneous frame is received correctly.
Source:
  If timeout or if NAK is received, retransmit that frame and all subsequent frames.
Examinable

## Slide 20: Go-Back-N: Max Window Size
Let us assume 3 bit sequencing, Window Size = 8
0
1
2
3
ACK 0
0
4
5
6
7
0
1
2
3
4
5
6
7
0 1 2 3 4 5 6 7 0 1 2 ..
0 1 2 3 4 5 6 7 0 1 2 ..
0
1
0 1 2 3 4 5 6 7 0 1 2 3 4 5 6 7 0 ..
0 1 2 3 4 5 6 7 0 1 2 3 4 5 6 7 0 ..
0 1 2 3 4 5 6 7 0 1 2 ..
Frame 0 is inserted at a wrong place. For this reason, maximum window size allowed is one less than that permitted by the sequence number. With k bit sequencing, maximum window size is 2k–1.
2
timeout
Examinable

## Slide 21: Go-Back-N: Max Window Size
0
1
2
3
0
1
2
3
0
4
5
6
4
5
6
0 1 2 3 4 5 6 7 0 1 2 ..
0 1 2 3 4 5 6 7 0 1 2 ..
0
1
0 1 2 3 4 5 6 7 0 1 2 3 4 5 6 7 0 ..
0 1 2 3 4 5 6 7 0 1 2 ..
ACK 7
Frame 0 is discarded.
NAK 7
0 1 2 3 4 5 6 7 0 1 2 3 4 5 6 7..
7
Let us assume 3 bit sequencing, Window Size = 7
timeout
Examinable

## Slide 22: Go-Back-N: Performance
Assumptions:
1. Tack and Tproc are negligible.
2. Frames are never completely lost on the medium.
3. ACKs and NAKs are never in error.
4. Each frame is (individually) acknowledged immediately.
This link utilization formula for Go-Back-N is complex, so we do not require you to
remember it. When you need to compute the link utilization for Go-Back-N,
you just use the link utilization formula for Selective Reject ARQ of Slide 27.
In other words, to simplify your computation, we consider
link utilization for Go-Back-N is the same as link utilization for Selective Reject ARQ.
Examinable

## Slide 23: Selective Reject ARQ: Illustration
receiver
sender
time
F
2
F
0
F
1
ACK
1
NA
K
1
F
3
F
4
F
1
AC
K
4
F
5
AC
K
5
AC
K
6
The sender will
only repeat
transmission
F
1
when NAK
1
is
received
The re
ceiver
expects
F
1
, but
F
2
arrives
instead. Hence
NAK1 is replied.
All received
frames will be
buffered before
F
1
arrives.
(
buffered
)
(buffered)
Efficient Scheme !
Examinable

## Slide 24: Selective Reject ARQ
Only rejected frames are retransmitted, (and of course those that time out).
Receiver informs transmitter of rejected frame n by sending ‘NAK n’ (‘Selective Reject n’ or simply ‘SREJ n’ in HDLC implementation)
After receiving an erroneous frame, subsequent frames are accepted by the receiver and buffered.
After receiving the valid copy of the error frame, frames are put in proper order and passed to the higher layer.
Minimizes retransmission.
Receiver requires more complex buffer management.
Examinable

## Slide 25: Selective Reject ARQ: Max Window Size
Let us assume 3 bit sequencing. Window Size = 5
0
1
2
3
4
0
ACK 5
Time-out
0 1 2 3 4 5 6 7 01 ..
0 1 2 3 4 5 6 7 0 1 2..
0 1 2 3 4 5 6 7 0 1 2 ..
0
1
2
3
4
0
The station assumes that frames 5, 6, & 7 have been lost, and it will accept frame 0, (and 1).
Conclusion: Window size of 5 cannot be permitted with 3 bit sequencing
Examinable

## Slide 26: Selective Reject ARQ: Max Window Size
Let us assume 3 bit sequencing, Window Size = 4.
0
1
2
3
0
ACK 4
Time-out
0 1 2 3 4 5 6 7 0 ..
0 1 2 3 4 5 6 7 0 1 ..
0
1
2
3
0
ACK 4
0 1 2 3 4 5 6 7 0 1 ..
Discard the frame, and send ACK again.
Conclusion: With k bit sequencing, max window size is 2k-1.
Examinable

## Slide 27: Selective Reject ARQ: Performance
P: Frame loss probability,
a: normalized propagation delay.
Since frame loss prob for each transmission is independent, in 1+2a time, we expect N transmissions, each with prob P of failure due to errors.
Setting P=0 reduces the above to that of Sliding Window.
Examinable

## Slide 28: Channel Utilization: Formulas
Stop-and-Wait ARQ
Sliding Window (no errors)
Selective Reject ARQ
Go-back-N ARQ
P: frame error probability
a: normalized propagation delay
N: window size
U: Channel Utilization (between 0 and 1)
This link utilization formula for Go-Back-N is complex, so we do not require you to
remember it. When you need to compute the link utilization for Go-Back-N,
you just use the link utilization formula for Selective Reject ARQ of Slide 27.
Examinable

## Slide 29: Learning Objectives
Stop-and-Wait ARQ
  To label frame flow
  Channel Utilization Calculation
Go-Back-N ARQ (GBN)
  To label frame flow
  To determine Max Window Size
Selective Reject ARQ (SR)
  To label frame flow
  To determine Max Window Size
  Link utilization calculation
  Comparison between GBN and SR