## Slide 1: Part I Syllabus – Fundamental Underlying Layers
Date​ | Subject​ | File​
Week 1:​ 9/Jan/2023​ 11/Jan/2023​ | Introduction: course logistics and Internet history​ | M1-L1-Introduction.pptx​
 | Layered Network Architecture​ | First part of M1-L2-Network Layer & Physical Resilience.pptx​
Week 2:​ 16/Jan/2023​ 18/Jan/2023​ | Physical Layer: Network Resilience​ | Second part of M1-L2-Network Layer & Physical Resilience.pptx​
 | Data link layer – Flow control​ | M1-L3-DLL-Flow Control.pptx​
Week 3:​​ 25/Jan/2023​ | Data link layer – Error control​ | M1-L4-DLL-Error Control.pptx​
Week 4:​ 30/Jan/2023​ 01/Feb/2023​ | Local area network – Introduction​ | M1-L5-LAN-Introduction.pptx​
 | Local area network – MAC​ | M1-L6-LAN-MAC.pptx​
Week 5:​ 06/Feb/2023​ 08/Feb/2023​ | Local area network – Ethernet​ | First part of M1-L7-LAN-Ethernet.pptx​
 | Local area network – Ethernet Evolutions​ | Second part of M1-L7-LAN-Ethernet.pptx​
Week 6:​ 13/Feb/2023​ 15/Feb/2023​ | Local area network – WLAN​ | M1-L8-LAN-WLAN.pptx​
 | Mobile Access Networks | M1-L9-Mobile.pptx
Week 7: 20/Feb/2023 22/Feb/2023 | E-learning for Network paradigms | M1-L10-Paradigms.pptx
 | Reviewing all contents taught in previous lectures | 

## Slide 2: Additional Materials
The related content talked today in https://eclass.teicrete.gr/modules/document/file.php/TP326/%CE%98%CE%B5%CF%89%CF%81%CE%AF%CE%B1%20(Lectures)/Computer_Networking_A_Top-Down_Approach.pdf is as follow:
  Chapter 5
https://www.techtarget.com/searchnetworking/definition/local-area-network-LAN

## Slide 3: Mingling Among a Cocktail party

## Slide 4: SC2008/CZ3006/CE3005 ​ Computer Network
Lecture 5
Local Area Network (LAN): Introduction

## Slide 5: Contents
Local Area Network
  Definition and Taxonomy
  Protocol Architecture
LAN Topologies
  Bus, Tree, Ring and Star
  Choice of topology
Transmission Media
Medium Access Control
  Functions and Features
  Static Channel Allocation
  Dynamic Channel Allocation

## Slide 6: Local Area Network (LAN)

## Slide 7: WAN/MAN/LAN
Not Examinable
hierarchical structure

## Slide 8: LAN (Local Area Networks)
LAN is a computer network that covers a small area (home, office, building, campus)
  a few kilometers
LANs (usually) do not involve leased lines; cabling and equipments belong to the LAN owner.
LAN consists of
  Shared transmission medium
    not so valid today due to switched LANs
  regulations for orderly access to the medium
  set of hardware and software for the interfacing devices
Not Examinable

## Slide 9: LAN Taxonomy
fiber
twisted pair
coax
wireless
bus
star
ring
tree
FDDI
Ethernet
Token ring
Wireless LAN
random access
token passing
polling
ANSI
IEEE 802
standard
bodies
transmission
media
Local Area Networks
products
MAC
protocols
topologies
Not Examinable

## Slide 10: LAN Protocol Architecture
Corresponds to lower two layers of OSI model
  But mostly LANs do not follow OSI model
Current LANs are most likely to be based on Ethernet protocols developed by IEEE 802 committee
IEEE 802 reference model
  Logical link control (LLC)
  Media access control (MAC)
  Physical
Not Examinable

## Slide 11: IEEE 802 Layers - Physical
Signal encoding/decoding
Preamble generation/removal
  for synchronization
Bit transmission/reception
Specification for topology and transmission medium
WiFi (Wireless Fidelity) vs. LiFi (Light Fidelity)
Not Examinable

## Slide 12: IEEE 802 Layers - DLL
OSI layer 2 (Data Link) is divided into two in IEEE 802
  Logical Link Control (LLC) layer
  Medium Access Control (MAC) layer
LLC layer
  Interface to higher levels
  flow control, error control
  Based on classical Data Link Control Protocols (so we have already covered it earlier)
MAC layer
  Prepare data for transmission
  Error detection
  Address recognition
  Govern access to transmission medium
    Not found in traditional layer 2 data link control
Not Examinable

## Slide 13: IEEE 802 Protocols vs OSI Model
Not Examinable

## Slide 14: LAN in a Nutshell
Physical Data Link
MAC LLC
IEEE 802.2
Logical Link Control Protocol
802.3 802.4 802.5 802.6 802.11 802.12 802.14
CSMA Token Token DQDB CSMA Round HFC
/CD Bus Ring /CA Robin
Coax Coax UTP Fiber Radio UTP Coax
UTP Fiber STP Infrared
STP Fiber
Fiber
B,T,S B,T,S R DB --- S, T T
Topologies (see next slide): Bus, Tree, Star, Ring, DualBus
Not Examinable
used by
Ethernet
used by
WiFi

## Slide 15: LAN Topologies
Not Examinable

## Slide 16: LAN Topologies: Bus, Tree, Ring and Star
Not Examinable

## Slide 17: Bus and Tree
Multipoint medium
Transmission propagates throughout medium
Heard by all stations
  Need to identify target station
    Each station has unique address
Full duplex connection between station and tap
  Allows for transmission and reception
Need to regulate transmission
  To avoid collisions
    If two stations transmit at same time, signals overlap
  To avoid continuous transmission from a single station.
    Solution: Transmit Data in small blocks – frames
Terminator absorbs frames at end of medium
Not Examinable

## Slide 18: Ring Topology
Repeaters are joined by point to point links in closed loop
  Receive data on one link and retransmit on another
  Links are unidirectional
  Stations attach to repeaters
Data Frames
  Circulate past all stations
  Destination recognizes address and copies frame
  Frame circulates back to source where it is removed
Medium access control determines when station can insert frame
Not Examinable

## Slide 19: Star Topology
Each station connected directly to central node
  using a full-duplex (bi-directional) link
Central node can broadcast (hub)
  Physical star, but logically like bus since broadcast
  Only one station can transmit at a time; otherwise, collision occurs
Central node can act as frame switch
  retransmits only to destination
  today’s technology
Not Examinable

## Slide 20: Choice of Topology
Reliability
Expandability
Performance
Needs considering in context of:
  Medium
  Wiring layout
  Access control
Not Examinable

## Slide 21: Transmission Medium
Not Examinable

## Slide 22: Medium Available (1)
Voice grade unshielded twisted pair (UTP)
  Cat 3/ Cheap
  Well understood
  Use existing telephone wiring in office building
  Low data rates
Shielded twisted pair (STP) and baseband coaxial
  More expensive than UTP but higher data rates
Broadband cable
  Still more expensive and higher data rate
Not Examinable

## Slide 23: Media Available (2)
Not Examinable
High performance unshielded twisted pair (UTP)
  Cat 5 and above (5e and 6)
  High data rate for small number of devices
  Switched star topology for large installations
Optical fiber
  Electromagnetic isolation
  High capacity
  Small size
  High cost of components
  High skill needed to install and maintain
Wireless Channel
  Fading channel

## Slide 24: Media Access Control (MAC)

## Slide 25: Media Access Control
Assembly of data into frame with address and error detection fields
Disassembly of frame
  Address recognition
  Error detection
Govern access to transmission medium
  Not found in traditional layer 2 data link control
For the same LLC, several MAC options may be available

## Slide 26: MAC Decision Making Options
Where?
  Central
    Greater control
    Simple access logic at station
    Avoids problems of co-ordination
    Single point of failure
    Potential bottleneck
  Distributed
How?
  Synchronous (static) solutions
    Specific capacity dedicated to connection
  Asynchronous (dynamic) solutions
    In response to demand

## Slide 27: Static Channel Allocation
TDM
FDM
Time Division Multiplexing (TDM)
  Each user is statically allocated one time slot
  if a particular user does not have anything to send, that period is wasted
  User may not utilize the whole channel for a time slot
Frequency Division Multiplexing (FDM)
  Channel is divided to carry different signals at different frequencies
  Efficient if there is a constant (one for each slot) amount of users with continous traffic
Code Division Multiplexing (CDM)
Not Examinable

## Slide 28: Dynamic Channel Allocation (1)
Round robin
  Each station has a turn to transmit
    declines or transmits up to a certain data limit
    overhead of passing the turn in either case
  Performs well if many stations have data to transmit for most of the time
    otherwise passing the turn would cause inefficiency
Reservation
  It is used for stream traffic, where time on the medium is divided into slots, much as with TDM.
  Reservation can be made in centralized or distributed fashion.
Not Examinable

## Slide 29: Dynamic Channel Allocation (2)
Contention
  All stations contend to transmit
  No control to determine whose turn is it
  Stations send data by taking risk of collision (with others’ packets)
    however they understand collisions by listening to the channel, so that they can retransmit
  Several implementation methods: Aloha, CSMA, etc
  In general, good for bursty traffic
    Typical traffic types for most networks
  Efficient under light or moderate load
  Performance is bad under heavy load
Not Examinable

## Slide 30: Learning Objectives
Local Area Network
  Functions of each layer: physical, LLC and MAC
  802 Protocol family
LAN Topologies
  Frame transmission over Bus, Tree, Ring and Star
Transmission Media
Medium Access Control
  Pros and Cons of Static Channel Allocation
  Comparison among Dynamic Channel Allocation