## Slide 1: Part I Syllabus – Fundamental Underlying Layers
Date​ | Subject​ | File​
Week 1:​ 9/Jan/2023​ 11/Jan/2023​ | Introduction: course logistics and Internet history​ | M1-L1-Introduction.pptx​
 | Layered Network Architecture​ | First part of M1-L2-Network Layer & Physical Resilience.pptx​
Week 2:​ 16/Jan/2023​ 18/Jan/2023​ | Physical Layer: Network Resilience​ | Second part of M1-L2-Network Layer & Physical Resilience.pptx​
 | Data link layer – Flow control​ | M1-L3-DLL-Flow Control.pptx​
Week 3:​​ 25/Jan/2023​ | Data link layer – Error control​ | M1-L4-DLL-Error Control.pptx​
Week 4:​ 30/Jan/2023​ 01/Feb/2023​ | Local area network – Introduction​ | M1-L5-LAN-Introduction.pptx​
 | Local area network – MAC​ | M1-L6-LAN-MAC.pptx​
Week 5:​ 06/Feb/2023​ 08/Feb/2023​ | Local area network – Ethernet​ | First part of M1-L7-LAN-Ethernet.pptx​
 | Local area network – Ethernet Evolutions​ | Second part of M1-L7-LAN-Ethernet.pptx​
Week 6:​ 13/Feb/2023​ 15/Feb/2023​ | Local area network – WLAN​ | M1-L8-LAN-WLAN.pptx​
 | Mobile Access Networks | M1-L9-Mobile.pptx
Week 7: 20/Feb/2023 22/Feb/2023 | E-learning for Network paradigms | M1-L10-Paradigms.pptx
 | Reviewing all contents taught in previous lectures | 

## Slide 2: Additional Materials
The related content talked today in https://eclass.teicrete.gr/modules/document/file.php/TP326/%CE%98%CE%B5%CF%89%CF%81%CE%AF%CE%B1%20(Lectures)/Computer_Networking_A_Top-Down_Approach.pdf is as follows:
  MAC protocols: page 445 - page 449
  ALOHA protocols: page 450 - page 453
  CSMA and CSMA/CD protocols: page 453 - page 459
You can also find video materials:
  ALOHA https://www.youtube.com/watch?v=j4-r0e7DjqY
  CSMA/CD https://www.youtube.com/watch?v=iKn0GzF5-IU

## Slide 3: How to mingle among cocktail
When to start speaking?
What to speak?
Whether/How to react to interruption?

## Slide 4: SC2008/CZ3006/CE3005 ​ Computer Network
Lecture 6
Medium Access Control (MAC) Protocols

## Slide 5: Contents
Medium Access Control Protocol
  Ideal MAC Protocol
  MAC Taxonomy
ALOHA Protocols
  Slotted ALOHA
  Pure ALOHA
CSMA Protocol
  Vulnerable time in CSMA
  CSMA Variants
CSMA/CD Protocol
  Collision Detection

## Slide 6: Medium Access Control Protocols
Single shared broadcast channel
Two or more simultaneous transmissions
  Collision if node receives two or more signals at the same time
MAC Protocol
  Distributed algorithm to share the channel
  Communication about channel sharing must use channel itself
    No out-of-band channel for coordination

## Slide 7: Ideal MAC Protocol
Broadcast Channel of Rate R-bps
  When one node transmits, it can send at rate R
  When M nodes want to transmit, each can send at average rate R/M
  Full decentralized
    No special node to coordinate transmissions
    No synchronization of clocks, slots
  Simple
  We call this ideal protocol as “genie-aided” MAC

## Slide 8: MAC Taxonomy
CSMA: Carrier Sense Multiple Access,
CSMA/CD: CSMA with Collision Detection,
CSMA/CA: CSMA with collision avoidance

## Slide 9: Random Access Protocols
When node has packet to send
  Transmits at full channel data rate of R
  No a-priori coordination among nodes
Two or more transmitting nodes
  Collision
Design of random MAC has 3 aspects
  Whether to sense channel status
  How to transmit frames
  How to detect and react to collision (What to do with the collision)

## Slide 10: ALOHA Protocols
aloha
/əˈləʊhə/
exclamation & noun
a Hawaiian word used when greeting or parting from someone.

## Slide 11: ALOHA
Inventor
  Norm Abramson
Assumptions
  All frames of the same size
  Time is divided into equal size slots, time to transmit 1 frame
  Nodes are synchronized
  Nodes start to transmit frames only at beginning of slots
  If 2 or more nodes transmit in slot, all nodes detect collision

## Slide 12: Slotted ALOHA
time

## Slide 13: Slotted ALOHA Efficiency
Result of a slot
  Successful (S): only one node transmits
  Collision (C): 2+ nodes transmits
  Empty (E): no transmission
If, there are N nodes and in each slot, each node transmits with probability p
  If a node i transmits, the probability that the transmission is successful is Pr(Si) = p (1-p)(N-1)
  The probability that a slot is successful is Pr(S) = Pr(S1) + Pr(S2) + … + Pr(SN) = N p (1-p)(N-1)

## Slide 14: Slotted ALOHA Efficiency
An example of 4-node network
  4 cases for a successful slot
Tx
No Tx
Case 1
Case 2
Case 3
Case 4
p(1-p)3
p(1-p)3
p(1-p)3
p(1-p)3
probability
Pr(S) = 4p(1-p)3

## Slide 15: Slotted ALOHA Efficiency
Offered load G = Np
  Expected total number of transmissions in a slot
Slotted ALOHA efficiency when N is large
*
**

## Slide 16: Slotted ALOHA Efficiency
  Pr(S) is throughput in frames per frame time
  Pr(S) <= 1/e (≈ 0.37) **
    1/e achieved when G = 1
    At the same time, Pr(E) ≈ 0.37, Pr(C) ≈ 0.26
** Tutorial 3.5
Chart: 
| 0 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013
ALOHA Efficiency | 0 | 0.090484 | 0.16375 | 0.22225 | 0.26813 | 0.30327 | 0.32929 | 0.34761 | 0.35946 | 0.36591 | 0.36788 | 0.36616 | 0.36143 | 0.35429 | 0.34524 | 0.3347 | 0.32303 | 0.31056 | 0.29754 | 0.28418 | 0.27067 | 0.25716 | 0.24377 | 0.2306 | 0.21772 | 0.20521 | 0.19311 | 0.18145 | 0.17027 | 0.15957 | 0.14936
Offered load G
Throughput
(1, 1/e)

## Slide 17: Pros and Cons of Slotted ALOHA
Pros
  Single active node can continuously transmit at full rate of channel
  Highly decentralized: only slots need to be sync
  Simple
Cons
  Collisions, wasting slots
  Empty slots
  Clock synchronization

## Slide 18: Pure ALOHA
In pure ALOHA, frames are transmitted at completely arbitrary times

## Slide 19: Pure ALOHA
Unslotted Aloha: simpler, no synchronization
When frame first arrives
  Transmit immediately
Collision probability increases:
  Frame sent at t0 collides with other frames sent in [t0-1, t0+1]

## Slide 20: Aloha Efficiency: Pure ALOHA
Pure Aloha: Partial transmission collision can occur (i.e., my 1st half of the transmission collides with your 2nd half)
Pr( success by given node) = P(node transmit) *
P( no other node transmits in [t0-1, t0]) *
P(no other node transmit in [t0, t0+1])
= p x (1-p)(N-1) x (1-p)(N-1)
= p (1-p)(2N-2)
  So for the network, Pr(S) = N p (1-p)(2N-2)
For very large N, Pr(S) = Ge-2G, where G=Np is the offered load
Therefore, Pr(S) <= 1/(2e) = 18.4%

## Slide 21: ALOHA Efficiency Comparison
S = throughput =(success rate)
G = offered load rate
= Expected total frames presented to the link per
the transmission time of a single frame
0.5
1.0
1.5
2.0
0.1
0.2
0.3
0.4
Pure Aloha
Slotted Aloha
Ge-G
Ge-2G

## Slide 22: Carrier-Sense Multiple-Access (CSMA)

## Slide 23: Carrier-Sense Multiple-Access
To improve performance, avoid transmissions that are certain to cause collisions
Based on the fact that in LAN propagation time is very small
  If a frame was sent by a station, all stations knows immediately so they can wait before start sending
  A station with frames to be sent, should sense the medium for the presence of another transmission (carrier) before it starts its own transmission
This can reduce the possibility of collision but it cannot eliminate it.
  Collision can only happen when more than one station begin transmitting within a short time (the propagation time period)

## Slide 24: CSMA Variants
Different CSMA protocols that determine:
  What a station should do when the medium is idle?
  What a station should do when the medium is busy?
Three Types of CSMA Protocols
  Non-persistent CSMA
  1-Persistent CSMA
  P-Persistent CSMA

## Slide 25: Non-persistent CSMA
A station with frames to be sent, should sense the medium
  If medium is idle, transmit; otherwise, go to 2
  If medium is busy, (backoff) wait a random amount of time and repeat 1
Non-persistent Stations are deferential (respect others)
Performance:
  Random delays reduces probability of collisions because two stations with data to be transmitted would wait for different amount of times.
  Bandwidth is wasted if waiting time (backoff) is large because medium will remain idle following end of transmission even if one or more stations have frames to send

## Slide 26: 1-Persistent CSMA
To avoid idle channel time, 1-persistent protocol used
Station wishing to transmit listens to the medium:
  If medium idle, transmit immediately;
  If medium busy, continuously listen until medium becomes idle; then transmit immediately with probability 1
1-persistent stations are selfish
Performance
  If two or more stations becomes ready at the same time, collision guaranteed

## Slide 27: P-Persistent CSMA
Time is divided to slots where each time unit (slot) typically equals maximum propagation delay
Station wishing to transmit listens to the medium:
  If medium idle,
    transmit with probability (p), OR
    wait one time unit (slot) with probability (1 – p), then repeat 1.
  If medium busy, continuously listen until idle and repeat step 1
Performance (wise guy)
  Reduces the possibility of collisions like non-persistent
  Reduces channel idle time like 1-persistent

## Slide 28: Flow Diagrams for CSMA

## Slide 29: CSMA Efficiency
Comparison of the channel utilization versus load for various random access protocols.

## Slide 30: CSMA/CD Protocol

## Slide 31: Collision in CSMA
A
1. A senses the medium idle and starts transmission
B
C
2. C senses the medium idle and starts transmission
3. Collision occurs at this place on the medium
Time
4. C detects the collision
5. A detects the collision

## Slide 32: Vulnerable Time in CSMA
Vulnerable time for CSMA is the maximum propagation time
The longer the propagation delay, the worse the performance of the protocol.

## Slide 33: CSMA/CD (Collision Detection)
CSMA has channel wastage
  If a collision has occurred, colliding packets are still to be fully transmitted.
CSMA/CD (Carrier Sense Multiple Access with Collision Detection) overcomes this:
  While transmitting, the sender is listening to medium for collisions.
  Sender stops transmission if collision has occurred, reducing channel wastage.
CSMA/CD is widely used for bus topology LANs (IEEE 802.3, Ethernet)

## Slide 34: How to detect a Collision?
Transceiver
  A node monitors the media while transmitting. If the observed power is higher than the transmitted power of its own signal, it means collision occurred.
Hub
  If input occurs simultaneously on two ports, it indicates a collision. Hub send a collision presence signal on all ports.

## Slide 35: Collision Detection
Question: How long does it take to detect a collision?
Answer: In the worst case, twice the maximum propagation delay of the medium
Note: a = maximum propagation delay

## Slide 36: CSMA/CD Protocol
Transmission protocol
  Use one of the CSMA persistent algorithms
If a collision is detected by a station during its transmission, it should do the following
  Abort transmission, and
  Transmit a jam signal (48 bits) to notify other stations of collision so that they will discard the transmitted frame also to make sure that the collision signal will stay until detected by the furthest station
  After sending the jam signal, backoff (wait ) for a random amount of time, then
  Transmit the frame again

## Slide 37: Learning Objectives
ALOHA Protocol
  Calculate throughput for ALOHA
  Maximize throughput by differentiation
CSMA Protocol
  Protocol comparison for three flavors
CSMA/CD Protocol
  Maximum duration for collision detection