## Slide 1: Part I Syllabus – Fundamental Underlying Layers
Week​ | Date​ | Subject​
Week 1 | 9/Jan/2023​ | Introduction: Course Logistics and Internet History​
 | 11/Jan/2023​ | Layered Network Architecture​
Week 2 | 16/Jan/2023​ | Physical-layer Resilience
 | 18/Jan/2023​ | Data Link Layer: Flow Control​
Week 3 | 25/Jan/2023​ (no class on 23/Jan/2023, a holiday​) | Data Link Layer: Error Control​
Week 4 | 30/Jan/2023​ | Local Area Network: Introduction​
 | 01/Feb/2023​ | Local Area Network: Medium Access Control (MAC)​
Week 5 | 06/Feb/2023​ | Local Area Network: Ethernet​
 | 08/Feb/2023​ | Local Area Network: Ethernet Evolutions​
Week 6 | 13/Feb/2023​ | Wireless Local Area Network (WLAN): Overview and 802.11
 | 15/Feb/2023​ | First Part: WLAN’s Multi-Access Reservation Protocol (MARP); Second Part: A Brief Overview of Network Paradigms​
Week 7 | 20/Feb/2023 | Network Paradigms​: Circuit Switching versus Packet Switching
 | 22/Feb/2023 | Mobile Access Networks

## Slide 2: Additional Materials
The related content talked today in https://eclass.teicrete.gr/modules/document/file.php/TP326/%CE%98%CE%B5%CF%89%CF%81%CE%AF%CE%B1%20(Lectures)/Computer_Networking_A_Top-Down_Approach.pdf is as follow:
  Ethernet: Page 469 – Page 476
  Frame: Page 537 – Page 541
You can also find other video materials about
  Ethernet
  MAC Addresses
  Frame Format
https://www.youtube.com/watch?v=MzhiVE6OuQA
https://www.youtube.com/watch?v=FkiTOMn-XGw
https://www.youtube.com/watch?v=jy4kBAzJCKM

## Slide 3: Network Engineer’s World
When we design our house
When we design our wedding rings

## Slide 4: SC2008/CZ3006/CE3005 ​ Computer Network
Lecture 7
Wired LAN: Ethernet

## Slide 5: Contents
Ethernet Overview
  Ethernet Standard
  Transmission Media
  Physical Layer
  Ethernet versions
Ethernet Frame Format
  Frame Format
  MAC Address
Ethernet MAC Protocol
  Minimum Frame Size
  Binary Exponential Backoff
Ethernet Evolution
  Bridged and Switched Ethernet
  Fast, Gigabit and Ten-Gigabit Ethernet
  Ethernet Pros and Cons

## Slide 6: Ethernet Overview

## Slide 7: Ethernet: A Brief History
History
  Invented by Bob Metcalfe and others at Xerox PARC in mid-1970s
  Roots in Aloha packet-radio network
  Standardized by Xerox, DEC, and Intel in 1978
  LAN standards define physical and MAC layers
    IEEE 802.3 (CSMA/CD - Ethernet) standard – originally 2Mbps
    IEEE 802.3u standard for 100Mbps Ethernet
    IEEE 802.3z standard for 1,000Mbps Ethernet
not examinable

## Slide 8: Ethernet Standard: Physical Layer
802.3 standard defines both physical and MAC layer details
  MAC Protocol: CSMA/CD
  Physical layer:
Metcalfe’s original
Ethernet Sketch: The idea was first documented in a memo that Metcalfe wrote on May 22, 1973, where he named it after the disproven luminiferous ether as an "omnipresent, completely-passive medium for the propagation of electromagnetic waves".
not examinable

## Slide 9: Ethernet Transmission Media
Coaxial cable
  Thick coax: Used by original Ethernet (bus topology)
  Thin coax: More flexible, but shorter network span
Twisted pair: For star topology, used with a hub, most commonly used
Optical fiber: Expensive, Fragile, Difficult to handle, but high data rate. Used in backbone.
twisted pair
coax
optical fiber
not examinable

## Slide 10: 802.3 Physical Layer Configurations
Physical layer configurations are specified in three parts
Data rate (10, 100, 1,000)
  10, 100, 1,000Mbps
Signaling method (base, broad)
  Baseband: digital signaling
  Broadband: analog signaling
Cabling (2, 5, T, F, S, L)
  2 – 200m thin coax
  5 – 500m thick coax (original Ethernet cabling)
  T – Twisted pair
  F – Optical fiber
  S – Short wave laser over multimode fiber
  L – Long wave laser over single mode fiber
not examinable

## Slide 11: Baseband Manchester Encoding
Baseband here means that no carrier is modulated; instead bits are encoded using Manchester encoding and transmitted directly by modifying voltage of a DC signal.
Manchester encoding ensures that a voltage transition occurs in each bit time which helps receiver in clock synchronization.
not examinable

## Slide 12: Ethernet Versions
Ethernet comes with several versions based on its network configurations. Important ones are:
  10BASE-5 (Original Ethernet)
  10BASE-2 (Cheapernet)
  10BASE-T (Star topology using a hub)
  Others (eg 10BASE-FL, 10BASE-FP, etc)
Notation:
10 BASE 5
10 Mbps
Signaling mode,
Base or Broad
Medium segment length (in 100m unit) or type. Possible options are: 5,2,T,F,etc
not examinable

## Slide 13: 10BASE-5
repeater
may add up to 4 more segments
Original Ethernet design, thick coax (50ohm) is used
Each segment is of 500m long (max)
Four repeaters (max) can be used to connect up to 5 segments
AUI cable connecting the PC and the thick coax cannot be longer than 50m
not examinable

## Slide 14: 10BASE-2
Called cheapernet because it is cheap to deploy. Thin coax is used
Each segment is of 185m long (max), min cable length between two computers is 0.5m, max 30 nodes
Up to 4 repeaters, (so entire network cable=925m)
not examinable

## Slide 15: 10BASE-T
‘T’ in 10BASE-T stands for Twisted pairs (UTP: unshielded twisted pairs). At least two pairs of wires.
Most popular Ethernet option
Cable length between a hub & a computer = 100m
not examinable

## Slide 16: Ethernet Frame Format

## Slide 17: Ethernet Frame Format
Preamble & SFD: 7 bytes with the pattern 10101010 followed by one byte with the pattern 10101011; used for synchronizing receiver to sender clock (clocks are never exact)
Pad field allows additional dummy data to be included to a frame for min. frame size requirement.
Frame Check Sequence field enables error detection using CRC. It covers between Source Address and Pad fields.
Ethernet frame

## Slide 18: Ethernet Frames
Preamble is a sequence of 7 bytes, each set to “10101010”
  Used to synchronize receiver before actual data is sent
Addresses
  unique, 48-bit unicast address assigned to each adapter
    example: 08:00:e4:b1:02:a2
    Each manufacturer gets their own address range
  broadcast: all 1s
  multicast: first bit (from right) of the first byte is 1
  unicast: first bit (from right) of the first byte is 0
Type field is a demultiplexing key used to determine which higher level protocol the frame should be delivered to
Body can contain up to 1500 bytes of data

## Slide 19: Broadcast, Multicast, Unicast
Broadcast: One to All
Multicast: One to Many
Unicast: One to One

## Slide 20: MAC Address Examples
Question
Define the type of the following destination addresses:
a. 4A:30:10:21:10:1A b. 47:20:1B:2E:08:EE
c. FF:FF:FF:FF:FF:FF
Solution
To find the type of the address, we need to look at the second hexadecimal digit from the left. If it is even, the address is unicast. If it is odd, the address is multicast. If all digits are F’s, the address is broadcast. Therefore, we have the following:
a. This is a unicast address because A in binary is 1010.
b. This is a multicast address because 7 in binary is 0111.
c. This is a broadcast address because all digits are F’s.

## Slide 21: Ethernet’s MAC

## Slide 22: Ethernet’s MAC Algorithm
Ethernet uses CSMA/CD
  Listens to line before/during sending
If line is idle (no carrier sensed)
  Send packet immediately
  Upper bound message size of 1500 bytes
  Must wait 9.6us between back-to-back frames
If line is busy (carrier sensed)
  Wait until idle and transmit packet immediately
    called 1-persistent sending
If collision detected
  Stop sending and jam signal
  Try again later

## Slide 23: Frame Collisions
Collisions are caused when two adaptors transmit at the same time (adaptors sense collision based on voltage differences)
  Both found line to be idle
  Both had been waiting for a busy line to become idle
A
B
A
B
A starts at
time 0
Message almost
there at time T when
B starts – collision!
How can we be sure A knows about the collision?

## Slide 24: Ethernet Minimum Frame Size
…
So, a sender must keep its transmission until it is sure that there are no other transmissions on the medium it is not aware of before it ends its transmission.
But then how long to keep its transmission?
A transmission requires an end-to-end signal propagation time (τ) to reach all stations (the longest), then a potential collision requires τ unit of time to return to the sender.
So the frame transmission ≥ 2τ; i.e., signal round trip time.
A
B
τ
+τ

## Slide 25: Collision Detection
How can A know that a collision has taken place?
  Must have a mechanism to ensure retransmission on collision
  A’s message reaches B at time T
  B’s message reaches A at time 2T
  So, A must still be transmitting at 2T
IEEE 802.3 specifies max value of 2T to be 51.2us
  This relates to maximum distance of 2500m between hosts
  At 10Mbps it takes 0.1us to transmit one bit so 512 bits (64B) take 51.2us to send
  So, Ethernet frames must be at least 64B long
    14B header, 46B data, 4B CRC
    Padding is used if data is less than 46B
Send jamming signal after collision is detected to ensure all hosts see collision
  48 bit signal

## Slide 26: Ethernet: Jam Signals
In the previous slide, B’s transmission cannot be too brief, otherwise A might not see the collision
To avoid this, a station is required to transmit a jam sequence (32 to 48 bits long) after it has detected a collision. This will make the collision more obvious.
A
1. A senses the medium idle and starts transmission
B
C
2. C starts a transmission
Time
3. C detects collision
4. C transmits jam signal
5. A detects collision, stops transmitting.
6. A sends jam signal

## Slide 27: Binary Exponential Backoff (BEB)
What should stations do when a collision is detected?
  Discard the packet and let upper layer protocols do the retransmission as in Aloha, slotted Aloha, and CSMA (☠ NO!!!!!). But how?
  They can choose a future slot randomly to retransmit based on Binary Exponential Backoff (BEB).
Delay time is selected using binary exponential backoff
  1st time: choose K from {0,1} then delay = K * 51.2us
  2nd time: choose K from {0,1,2,3} then delay = K * 51.2us
  nth time: delay = K x 51.2us, for K from {0,1,… 2n – 1}
    Note max value for K = 1023
  give up after several tries (usually 16)
    Report transmit error to host
If delay were not random, then there is a chance that sources would retransmit in lock step
Why not just choose from small set for K
  This works fine for a small number of hosts
  Large number of nodes would result in more collisions

## Slide 28: BEB: Example
Channel
A
B
0
1
0
1
2
3
1st Retrial
P(Collision) = P(A&B=0) + P(A&B=1)
P(A&B=0) = P(A=0)*P(B=0)
= 0.5*0.5 = 0.25
P(Collision) = 0.25 +0.25 =0.5
2nd Retrial
P(Collision) = P(A&B=0) + P(A&B=1)
+ P(A&B=2) + P(A&B=3)
P(A&B=0) = P(A=0) * P(B=0)
= 0.25 * 0.25 = 0.0625
P(Collision) = 4*0.0625 = 0.25

## Slide 29: MAC Algorithm from Receiver
Senders handle all access control
Receivers simply read frames with acceptable address
  Address to host
  Address to broadcast
  Address to multicast to which host belongs
  All frames if host is in promiscuous mode

## Slide 30: Ethernet Evolutions

## Slide 31: Collision Domain
Network region in which collisions are propagated.
  Repeaters (2-port) and hubs (multi-port) propagate collisions.
  Bridges (2-port), switches (multi-port) and routers do not.
Collision frequency can be kept low by breaking the network into segments bounded by:
  bridges
  switches
  routers
Read https://www.geeksforgeeks.org/network-devices-hub-repeater-bridge-switch-router-gateways/

## Slide 32: Broadcast Domain
Network region in which broadcast frames are propagated.
  Repeaters, hubs, bridges, & switches propagate broadcasts. (Layer 2)
  Routers either do or don’t, depending on their configuration.(Layer 3)
Broadcasts are necessary for network function.
Some devices and protocols produce lots of broadcasts; avoid them.
Broadcast frequency can be kept manageable by limiting the LAN size.
LANs can then be cross-connected by routers to make a larger internetwork.

## Slide 33: Bridged Ethernet

## Slide 34: Shared versus Switched
...
destination
hub
A repeater (or a hub) forwards the received signals to all output ports except the incoming port.
A collision occurs when two computers transmit at the same time. In this case, the channel carries no useful information.
...
sender
destination
switch
A switch (or a switching hub) forwards the received signals only to the destination.
When two transmissions arrive at the switch at the same time, they will be stored in different buffers so that their frames can be forwarded later. No collision is resulted.
...

## Slide 35: Switched Ethernet
Switches forward and filter frames based on LAN addresses
  It’s not a bus or a router (simple forwarding tables are maintained)
Very scalable
  Options for many interfaces
  Full duplex operation (send/receive frames simultaneously)
Connect two or more “segments” by copying data frames between them
  Switches only copy data when needed
    key difference from repeaters
Higher link bandwidth
  Collisions are completely avoided
Much greater aggregate bandwidth
  Separate segments can send at once
not examinable

## Slide 36: Fast Ethernet (FE)
Fast Ethernet (100Mbps) has technology very similar to 10Mbps Ethernet
  Uses different physical layer encoding (4B5B)
  Many NIC’s are 10/100 capable
    Can be used at either speed
Summary of Fast Ethernet Implementation
not examinable

## Slide 37: Gigabit Ethernet (GbE)
Gigabit Ethernet (1,000Mbps)
  Compatible with lower speeds
  Uses standard framing and CSMA/CD algorithm
  Distances are severely limited
  Used for backbones and inter-router connectivity
  Cost competitive
not examinable

## Slide 38: Ten-Gigabit Ethernet (10GbE)
Ten-Gigabit Ethernet (10Gbps)
  Defined by IEEE 802.3ae-2002
  Higher-grade copper cables required: cat 6a or Class F/Cat 7 cables for links up to 100m
not examinable

## Slide 39: Ethernet Adoption Trends
http://www.cisco.com/c/en/us/products/collateral/switches/catalyst-6500-series-switches/white_paper_c11-696667.html
not examinable

## Slide 40: Experiences with Ethernet
Ethernets work best under light loads
  Utilization over 30% is considered heavy
    Network capacity is wasted by collisions
Most networks are limited to about 200 hosts
  Specification allows for up to 1024
Most networks are much shorter
  5 to 10 microsecond RTT
Transport level flow control helps reduce load (number of back to back packets)
Ethernet is inexpensive, fast and easy to administer!
not examinable

## Slide 41: Ethernet Problems
Ethernet’s peak utilization is pretty low (like Aloha)
Peak throughput worsens with
  More hosts
    More collisions
  Longer links
    Collisions take longer to observe, more wasted bandwidth
Efficiency can be improved by avoiding the above conditions
not examinable

## Slide 42: Why did Ethernet win?
There are many LAN protocols (ARCNET, Token ring, AppleTalk, etc)
  Price
  Performance
  Availability
  Ease of use
  Scalability
not examinable

## Slide 43: Learning Objectives
Ethernet Overview
  Read Ethernet versions
Ethernet Frame Format
  Understand MAC address: unicast/broadcast
Ethernet MAC Protocols
  Calculate minimum frame size
  Calculate collision rate under BEB scheme
Ethernet Evolutions
  Count collision/broadcast domains
  FE/GbE/10GbE
not examinable
examinable
examinable
examinable
examinable
not examinable

## Slide 44: Practice
1. Go to www.menti.com and use the code 6743 9603
2. Go to www.menti.com and use the code 4659 5518