## Slide 1: Part I Syllabus – Fundamental Underlying Layers
Date​ | Subject​ | File​
Week 1:​ 9/Jan/2023​ 11/Jan/2023​ | Introduction: course logistics and Internet history​ | M1-L1-Introduction.pptx​
 | Layered Network Architecture​ | First part of M1-L2-Network Layer & Physical Resilience.pptx​
Week 2:​ 16/Jan/2023​ 18/Jan/2023​ | Physical Layer: Network Resilience​ | Second part of M1-L2-Network Layer & Physical Resilience.pptx​
 | Data link layer – Flow control​ | M1-L3-DLL-Flow Control.pptx​
Week 3:​​ 25/Jan/2023​ | Data link layer – Error control​ | M1-L4-DLL-Error Control.pptx​
Week 4:​ 30/Jan/2023​ 01/Feb/2023​ | Local area network – Introduction​ | M1-L5-LAN-Introduction.pptx​
 | Local area network – MAC​ | M1-L6-LAN-MAC.pptx​
Week 5:​ 06/Feb/2023​ 08/Feb/2023​ | Local area network – Ethernet​ | First part of M1-L7-LAN-Ethernet.pptx​
 | Local area network – Ethernet Evolutions​ | Second part of M1-L7-LAN-Ethernet.pptx​
Week 6:​ 13/Feb/2023​ 15/Feb/2023​ | Local area network – WLAN​ | M1-L8-LAN-WLAN.pptx​
 | Mobile Access Networks | M1-L9-Mobile.pptx
Week 7: 20/Feb/2023 22/Feb/2023 | E-learning for Network paradigms | M1-L10-Paradigms.pptx
 | Reviewing all contents taught in previous lectures | 

## Slide 2: Which one is more valuable?

## Slide 3: SC2008/CZ3006/CE3005 Computer Network
Lecture 2
Network Layers and Physical Resilience

## Slide 4: Contents
Layered Network Architecture
  Motivations and Benefits
  OSI 7-Layer Model
  Internet 5-Layer Implementation (i.e., TCP/IP)
Physical Resilience
  Link Failure probability
  Network resilience calculation

## Slide 5: Layered Network Architecture

## Slide 6: Motivations for Layered Network Architecture
Networks are complex with many pieces
  Hosts, routers, links, applications, protocols, hardware, software
Dealing with complex systems
  Explicit structure allowing identification, relationship of different pieces
    Layered reference model for discussion
  Modularization easing maintenance and updating
    Change of layer’s service transparent to rest of system
    Change in network technology does not affect rest of system
  Layering (design vs implementation)

## Slide 7: A Layered Example for Web
Browser requests web page from server
Server determine if access is granted
Reliable transfer page from server to client
Physical transfer of bits from server to client

## Slide 8: Layered Network Architecture
Network organized as a stack of layers
  Purpose of layer is to offer services to the layer above it and passes data & control information to the layer below, using a well-defined interface
  Reducing design complexity
Protocols: a set of rules governing communication between two peering parties/computers
  define format, order of messages sent and received among network entities, and actions taken on message transmission & receipt.
Network Architecture: a set of layers and protocols with specifications enabling hardware/software developers to build systems compliant with a particular architecture

## Slide 9: Benefits of Layers
Simplicity
  Easy to design once layers and their interactions are defined clearly
Flexibility
  Easy to modify and develop networks by separate layers modifications
Incremental Changes
  Easy to add new layers, add new functions to a layer

## Slide 10: OSI 7-Layer Model
Function Decomposition
  Weakly-decoupled stack
Encapsulation
  Each layer adding new headers
Peering
  Only peer layer “communicating” with each other

## Slide 11: OSI Reference Model: 7 Layers (More on Supplementary Materials)
OSI Model |  |  | 
 | Data unit | Layer | Function
Host layers | Data | 7. Application | Network process to application
 |  | 6. Presentation | Data representation, encryption and decryption, convert machine dependent data to machine independent data
 |  | 5. Session | Inter-host communication, managing sessions between applications
 | Segment | 4. Transport | End-to-end connections, reliability and flow control
Media layers | Packet | 3. Network | Path determination and logical addressing
 | Frame | 2. Data link | Physical addressing
 | Bit | 1. Physical | Media, signal and binary transmission

## Slide 12: OSI in Action: Encapsulation
A message begins at the top application layer and moves down the OSI layers to the bottom physical layer
As the message descends, each successive OSI model layers adds a header to it
A header is layer-specific information that basically explains what functions the layer carries out
Conversely, at the receiving end, headers are stripped from the message as it travels up the OSI layers.

## Slide 13: A Simple Computer Network
Your NTU Computer
SG Net Core
Undersea Cable
USA Net Core
USA guy
Packet Switched Network
(i.e., Network Core)

## Slide 14: Header Processing at Switch Node

## Slide 15: OSI Unified View: Protocols
Layer n in one machine interacts with layer n in another machine to provide a service to layer n +1
The entities comprising the corresponding layers on different machines are called peer processes.
The machines use a set of rules and conventions called the layer-n protocol.
Layer-n peer processes communicate by exchanging Protocol Data Units (PDUs)
n
Entity
n
Entity
Layer n peer protocol
n-PDUs
Not Examinable

## Slide 16: OSI Unified View: Services
Communication between peer processes is virtual and actually indirect
Layer n+1 transfers information by invoking the services provided by layer n
Services are available at Service Access Points (SAP’s)
Each layer passes data & control information to the layer below it until the physical layer is reached and transfer occurs
The data passed to the layer below is called a Service Data Unit (SDU)
SDU’s are encapsulated in PDU’s
Not Examinable

## Slide 17: Layers, Services & Protocols
n+1
entity
n-SAP
n+1
entity
n-SAP
n entity
n entity
n-SDU
n-SDU
n-SDU
H
H
n-SDU
n-PDU
Not Examinable

## Slide 18: OSI Model in a Nutshell
Not Examinable

## Slide 19: TCP/IP Model: 5 Layers
Application: supporting network applications
  FTP, SMTP, HTTP
Transport: host-host data transfer
  Transmission Control Protocol (TCP), UDP
Network: routing of datagrams from source to destination
  Internet Protocol (IP), routing protocols
Link: data transfer between neighboring network elements
  PPP, Ethernet
Physical: bits on the wire

## Slide 20: TCP/IP Internetworking
Each layer takes data from above
  Adds header information to create new data unit
  Passes new data unit to layer below
router

## Slide 21: TCP/IP vs OSI Models
Part II
Part I
CE/CZ4023

## Slide 22
Part I Syllabus
Date​​ | Subject​​ | File​​
Week 1:​​ 9/Jan/2023​​ 11/Jan/2023​​ | Introduction: course logistics and Internet history​​ | M1-L1-Introduction.pptx​​
 | Layered Network Architecture​​ | First part of M1-L2-Network Layer & Physical Resilience.pptx​​
Week 2:​​ 16/Jan/2023​​ 18/Jan/2023​​ | Physical Layer: Network Resilience​​ | Second part of M1-L2-Network Layer & Physical Resilience.pptx​​
 | Data link layer – Flow control​​ | M1-L3-DLL-Flow Control.pptx​​
Week 3:​​ 23/Jan/2023​​ 25/Jan/2023​​ | Data link layer – Error control​​ | M1-L4-DLL-Error Control.pptx​​
 | Local area network – Introduction​​ | M1-L5-LAN-Introduction.pptx​​
Week 4:​​ 30/Jan/2023​​ 01/Feb/2023​​ | Local area network – MAC​​ | M1-L6-LAN-MAC.pptx​​
 | Local area network – Ethernet​​ | First part of M1-L7-LAN-Ethernet.pptx​​
Week 5:​​ 06/Feb/2023​​ 08/Feb/2023​​ | Local area network – Ethernet Evolutions​​ | Second part of M1-L7-LAN-Ethernet.pptx​​
 | Local area network – WLAN​​ | M1-L8-LAN-WLAN.pptx​​
Week 6:​​ 13/Feb/2023​​ 15/Feb/2023​​ | Mobile Access Networks: From 1G to 5G ​​ | M1-L9-Mobile.pptx​​
 | Network paradigms​​ | M1-L10-Paradigms.pptx​​

## Slide 23: Physical Layer: Network Resilience

## Slide 24
Use links for abstraction

## Slide 25: GMT 12:26:01, 26 December 2006
Taiwan
7.1 magnitude quake
Multiple aftershocks
6 cable systems effected

## Slide 26
M
N
Qingdao
N
East Asia Crossing (EAC) Cable Network
Here the network topology is like a mesh,
so it is quite resilient.
A mesh network intuitively means there are
multiple paths between any two nodes.

## Slide 27
City-to-City (C2C) Cable Network
Singapore
Batangas
S4
Tanshui
Pusan
Chikura
Shima
Hong Kong
S3a
Shanghai
Fungshan
S3b
S3c
S5
S6
S7
S1
S2a
S2c
S2b
Ring
Line
with a link broken becomes
Here the network topology is like a ring,
so it is not that resilient.

## Slide 28
Tanshui
Pali
Fangshan
Shanghai
Shantou
Philippines
Miyazaki
APCN-2
S6
S7
S4
S3
S2
S8
SMW3
Okinawa
Macau
Other Cable Network
China-US
N3
S1
N2
W3
N1
W1
W2
N4
N5
N9
N6
N7
N8
S2
S3
S4
S5
FNAL/RNAL
Flag
Philippines
B3
B5
B2
B8
B1
B4
B17
B6
B7
B9
APCN
Toucheng
Here the network topology is like a ring,
so it is not that resilient.
Here the network topology is like a bus,
so it is not that resilient.
Ring/bus is less resilient than mesh,
but cheaper.

## Slide 29: Network Reliability
Probability that a network performs satisfactorily over a period of time
Parameters:
  Mean Time Between Failures (MTBF)
  Mean Time to Failure (MTTF)
  Mean Time to Repair (MTTR)
MTBF = MTTF + MTTR
Operation
MTTF
MTTR
time

## Slide 30: Link Failure Probability
Link Failure Probability: percentage of time during which the link is dysfunctional
Link Availability: percentage of time during which the link is functional
bi : Probability link “i” is broken
ri : Probability link “i” is available, i.e., not broken
ri = 1 - bi

## Slide 31: Network Resilience Issues
What’s the probability of a link failure?
Are there alternative paths?
Is there a single point of failure ?
What is the probability for two nodes to stay connected in a network?

## Slide 32: Network Resilience
A measure of Network Fault Tolerance
Express in terms of probability that the network remains connected.
Assumptions
  The probability of link failures are independent of each other.

## Slide 33: Network Availability: Single Link
SG
AU
Given that the failure probability of the link is 0.05,
Failure probability: bSG-AU = 0.05
Availability probability: rSG-AU = 1-0.05 = 0.95

## Slide 34: Network Availability: Series
Given that each link has a failure probability of 0.05,
rSG-HW-AU = Pr [both links survive] = rSG-HW * rHW-AU = (1-0.05)*(1-0.05)
= 0.9025
bSG-HW-AU = 1-0.9025 = 0.0975
What is the probability that SG cannot communicate with AU?
Computing 1 - rSG-HW * rHW-AU above is easier than summing the three products below:
bSG-HW * bHW-AU
SG
AU
HW
SG
AU
HW
SG
AU
HW
bSG-HW * rHW-AU
rSG-HW * bHW-AU
SG
AU
HW
Prob that SG can communicate with AU:

## Slide 35: Network Availability: Parallel
AU
Given that each link has a failure probability of 0.05,
What is the probability that SG is isolated from AU ?
Link B
SG
Prob(break) = Pr[both links break]
= bA * bB
= 0.05 * 0.05 = 0.0025
SG
AU
bSG-AU = 0.0025

## Slide 36: Hybrid Graphs: Path-Based Approach
Given that each link has a failure probability of 0.05,
Calculate the Prob that SG is isolated from AU.
rSG-HW-AU = rSG-HW * rHW-AU
= (1-0.05)*(1-0.05)
= 0.9025
AU
HW
SG
0.05
0.05
0.05
bSG-HW-AU = 1- rSG-HW-AU
= 1-0.9025
= 0.0975
Prob. SG Disconnected from AU = bSG-HW-AU * bSG-AU
= 0.0975 * 0.05
= 0.004875

## Slide 37: Rules for Network Availability
Link in series
  Calculate that probability that all links in the series are working
Link in parallel
  Calculate the probability that all links are broken.
Combination of series and parallel
  Decompose them into paths
  Calculate network availability using path-based approach

## Slide 38: Learning Objectives
Layered Network Architecture
  Why layering?
  OSI model and its functions
  TCP/IP model and its functions
  Mapping between OSI and TCP/IP Models
Physical Layer Resilience
  Definition of link availability and calculation
  Path-based approach

## Slide 39: Supplementary Materials
Remark:
For the supplementary materials in the lecture notes, they are not examinable but as the reference for you to better understand the lecture.
However, some of the content in the supplementary may appear in other slides (not in the supplementary). And if so, this content is examinable.

## Slide 40: Physical Layer
Provides physical interface for transmission of information
Defines rules by which bits are passed from one system to another on a physical communication medium
Covers all – mechanical, electrical, functional and procedural – aspects for physical communication
Such characteristics as voltage levels, timing of voltage changes, physical data rates, maximum transmission distances, physical connectors, and other similar attributes are defined by physical layer specifications

## Slide 41: Data Link Layer
Data link layer attempts to provide reliable communication over the physical layer interface
Breaks the outgoing data into frames and reassemble the received frames
Create and detect frame boundaries
Handle errors by implementing an acknowledgement and retransmission scheme
Implement flow control
Supports points-to-point as well as broadcast communication
Supports simplex, half-duplex or full-duplex communication

## Slide 42: Network Layer
Implements routing of frames (packets) through the network
Defines the most optimum path the packet should take from the source to the destination
Defines logical addressing so that any endpoint can be identified
Handles congestion in the network
Facilitates interconnection between heterogeneous networks (Internetworking)
The network layer also defines how to fragment a packet into smaller packets to accommodate different media

## Slide 43: Transport Layer
Purpose of this layer is to provide a reliable mechanism for the exchange of data between two processes in different computers
Ensures that the data units are delivered error free
Ensures that data units are delivered in sequence
Ensures that there is no loss or duplication of data units
Provides connectionless or connection oriented service
Provides for the connection management
Multiplex multiple connection over a single channel

## Slide 44: Session Layer
Provides mechanism for controlling the dialogue between the two end systems. It defines how to start, control and end conversations (called sessions) between applications
Requests for a logical connection to be established on an end-user’s request
Any necessary log-on or password validation is also handled by this layer
Session layer is also responsible for terminating the connection
This layer provides services like dialogue discipline which can be full duplex or half duplex
Session layer can also provide check-pointing mechanism such that if a failure of some sort occurs between checkpoints, all data can be retransmitted from the last checkpoint

## Slide 45: Presentation Layer
Presentation layer defines the format in which the data is to be exchanged between the two communicating entities
Also handles data compression and data encryption (cryptography)

## Slide 46: Application Layer
Application layer interacts with application programs and is the highest level of OSI model
Application layer contains management functions to support distributed applications
Examples of application layer are applications such as file transfer, electronic mail, remote login etc.