## Slide 1: Chapter 6: Modular Programming-Cont Lecture 2 (live)
Mohamed M. Sabry Aly
N4-02c-92

## Slide 2: System Stack
A stack is a first-in, last-out linear data structure that is maintained in the memory’s data area.
The system stack in the ARM processor is maintained by a dedicated stack pointer (SP, R13).
Stack can grow towards lower or higher memory address
  Preferred direction is lower, start from max address
E.G. Stack growing lower address
SP
Memory map
0x000
0xFFF
System stack
Item #n-1
Item #n (top)
The SP points to the top item on the system stack.
The 3 basic stack operations are push, pop and access items on the stack.
Ref: Null & Lobur (3rd Ed) section A.2.3 – Stacks
0xF00
0xEFC
0xEF8
SP
SP

## Slide 3: Push Data to the Stack
Writing to stack can be done using STR instruction
  Need to also increase the stack pointer before storing
Syntax: STR R0, [SP,#-4]!
0xEF8
0xEFC
0xF00
0xF04
Memory map
(stack area)
0x0F00
SP
0x000
R0
Before execution
0xEF8
0xEFC
0xF00
0xF04
Memory map
(stack area)
0xF00
SP
0x0000
R0
SP
0x1234
0x5678
0x89AB
0xCDEF
0x1234
0x5678
0x89AB
0xCDEF
SP
0000
SP
0xEFC
After execution
0xEFC
0000

## Slide 4: Pop Data off the Stack
Popping from the stack can be done with LDR instruction
  Need to update pointer AFTER read
Syntax: LDR R0, [SP],#4
Memory map
(stack area)
0xEFC
SP
0x0000
R0
Before execution
0xEF8
0xEFC
0xF00
0xF04
Memory map
(stack area)
0xEFC
SP
0x0000
R0
SP
0x1234
0x5678
0x89AB
0xCDEF
0x1234
0x5678
0x89AB
0xCDEF
SP
5678
SP
After execution
F00
F00
5678
Add 4
Remove from stack
0xEF8
0xEFC
0xF00
0xF04

## Slide 5: Removing from stack
After popping, is the data erased from the stack?
  NO
Data still resides in memory and can be read
  LDR R0, [SP, #-4]
0x1234
0x5678
0x89AB
0xCDEF
0xEF8
0xEFC
0xF00
0xF04
SP is not changed

## Slide 6: Pushing Registers to Stack
E.g., want to push R0 and R1
Method 1:
STR R0, [SP, #-4]!
STR R1, [SP, #-4]!
Method 2:
STMFD SP!,{R1,R0}
Store multiple registers fully descending
Use Stack pointer and write back updated value after operation
Write registers in descending order
Memory map
(stack area)
0xF00
SP
SP
0x1234
0x5678
0x89AB
0xCDEF
0xEF8
0xEFC
0xF00
0xF04
Before Execution
Memory map
(stack area)
0xEF8
SP
SP
R0
R1
0x89AB
0xCDEF
0xEF8
0xEFC
0xF00
0xF04
After Execution

## Slide 7: Pushing and popping to stack
STMFD SP!, {list of registers}
LDMFD SP!, {list of registers}
STMFD SP!,{R1,R0}
LDMFD SP!,{R1,R0}

## Slide 8: Parameter Passing using Stack
Most general method of parameter passing – no registers needed, supports recursive programming.
Large numbers of parameters can be passed as long as stack does not overflow.
Parameter passing using the stacks
Calling program
SUB1
:
Get parameters
From the stack
:
MOV PC,LR
BL SUB1
Subroutine
Setup parameters in stack
Parameters are pushed onto the stack before calling the subroutine and retrieved from the stack within the subroutine.

## Slide 9: Parameter Passing using Stack
Parameters pushed to the stack must be removed by the calling program immediately after returning from subroutine.
If not, repeated pushing of parameters to the stack will lead to a stack overflow.
Parameter passing using the stacks
Calling program
SUB1
:
Get parameters
From the stack
:
MOV PC, LR
BL SUB1
Subroutine
Setup parameters in stack
Remove parameters
from stack

## Slide 10: Review Q4 – Stack Passing
(1)
(2)
(3)
(4)
Show the known contents on the stack on entering subroutine SubA.
(2)
(3)
(4)
MOV R0,#0x100
LDR R1,[R0],#4
STMFD SP!,{R1,R0}
BL SubA
:
Memory
Address
0x100
0x104
:
0x008
0x003
:
Address
0x000
0x004
0x008
0x00C
0x010
Free Stack Space
0x008
SP
0x104
Free Stack Space
0x104
SP
0x008
(1)
Free Stack Space
0x104
SP
0x003
Free Stack Space
0x100
SP
0x008

## Slide 11: Sum from 1 to N
Write a subroutine to:
Sum the positive numbers from 1 to N, where N is a value passed to the subroutine.
The computed sum should be directly updated to a memory variable Answer, whose address is 0x100.
Solution:
Push two parameters on stack, the value of N and address of memory variable Answer.
???
Answer
Data Memory
0x100
0x104
0x108
All parameters are to be passed via the stack.

## Slide 12: Calling the Subroutine
???
Answer
Data Memory
0x100
0x101
0x102
SP
Remove parameters
from the Stack
: ;find the sum of (1+2+3+4+5), where N=5
MOV R1, #5 ;Set R0 with #5
MOV R0, #0x100 ;Set R1 with the address
STMFD SP!, {R1,R0} ;push R0&R1 to stack
BL Sum1N ;call subroutine Sum1N
:
Free Stack Space
Items on the stack
SP
+8
Parameters setup
ADD SP,SP,#8 ;add 8 to pop the two parameters from stack
N=5
Address
(of Answer)
SP
Equivalent to
LDMFD SP!,{r1,r0}

## Slide 13: Sum from 1 to N Subroutine Possible Solution
Note: The subroutine needs three registers. R4 to compute the sum from 1 to N. R6 to be an address pointer to the memory variable Answer where the results will written to. R5 holds the value of N, which is decremented by 1 after each loop till it reaches 0.
Sum1N STMFD SP!,{R4,R5,R6} ;save registers to stack
LDMFD SP!,{R4,R5,R6} ;restored saved registers
MOV PC,LR ;return from subroutine

Compute Sum from 1 to N here

LDR R5,[SP,#16] ;Load N from stack to R5
LDR R6,[SP,#12] ;Load Answer’s From stack
Retrieve stack parameters
MOV R4,#0 ;clear summation register R0 to 0
Loop ADD R4,R4,R5 ;add current value in R5 to R4
SUBS R5,R5,#1 ;decrement current value in R4 by 1
BNE Loop ;jump back to Loop if R4 not yet zero
STR R4,[R6] ;write sum to Answer
R4 = R4 + R5
R5 decrements from N to 0 with each loop, thereby summing 1 to N.
Free Stack Space
Items on the stack
N=5
Answer
Answer Addr
R6
N
R5
N
Write result in R4 directly to Answer
Answer Addr

## Slide 14: Sum from 1 to N Subroutine Accessing Stack Parameters
Note: SP indirect with offset can be used to access parameters on the stack but knowledge of all items on the stack is needed to compute the correct offset from the current SP position.
After SP
3
After SP
1
Memory map
(stack area)
0xFDC
0xFE0
0xFE4
0xFE8
0xFEC
0xFF0
Address (of Answer)
N=5
Saved R6
Saved R5
:
STMFD SP!,{R1,R0}
BL Sum1N
Calling program
1
2
Subroutine Sum1N
STMFD SP!,{R4-R6} LDR R5,[SP,#16]
LDR R6,[SP,#12]
3
Before SP
1
SP+0
SP+4
SP+8
SP+12
SP+16
SP+20
Offset from SP
Displacements for stack parameters
Saved R4

## Slide 15: What should be the instruction in a
LDMFD SP, {R5,R4}
LDMFD SP!, {R5,R4}
LDMFA SP, {R4,R5}
LDMFA SP!, {R4,R5}
SubX STMFD SP!,{R5,R4} LDR R4,[SP,#12]
LDR R5,[SP,#8]
:
:
:
; (a)
MOV PC,LR

## Slide 16: Transparent Subroutines
To achieve this, all local registers used by the subroutine (R4-R11) must be saved on the stack on entry and restored from stack before returning.
A transparent subroutine will not affect any CPU resources used by the program calling it.
SUB1
:
: ; registers R4 to R7 are
: ; used in subroutine
MOV PC,LR ; return to calling program
LDMFD SP!,{R4-R7} ; restore R4 to R7 from stack
MOV R4,#0xFFFFFFFF
Calling program
:
MOV R4,#0
BL SUB1
What is in R4 here?
:
@#!*&
STMFD SP!,{R4-R7} ; save R4 to R7 to stack
Modify R4 to -1

## Slide 17: For the shown code segment, how are parameters A and B passed?
A reference, B value
A value, B value
A reference, B reference
A value, B reference
MOV R0,#0x100
LDR R1,[R0],#4
STMFD SP!,{R0,R1}
BL Sub
A
B
0x100
0x104

## Slide 18: Passing by value and by reference
Parameters are passed to subroutines in 2 ways:
Pass by value – the value of the data (or variable) is passed to the subroutine.
When the parameter passed is to be modified by the subroutine.
Large quantity of data (e.g. array) have to be passed between subroutine and calling program.
When is passing by reference used?
MOV R1,#5
MOV R0,#0x100
STMFD SP!,{R1,R0}
BL Sum1N
Calling program
Pass by reference – the address of the variable is passed to the subroutine .

## Slide 19: C Function Example
C function to compute the mean value of N elements in an integer Array.
Note: Observe that local variables are required by the function to compute the result.
int Mean (int *Array, int N)
{
int avg, i;
int sum = 0;
for (i=0; i<N; i++)
sum = sum + Array[i];
avg = sum / N;
return avg;
}
Passing by reference
Passing by value
Local variables used only by the function
Function’s single output is normally
returned via the R0 (or R12) register

## Slide 20: C Function Example
C function to compute the mean value of N elements in an integer Array.
Pass both parameters by reference.
Note: Observe that local variables are required by the function to compute the result.
int Mean (int *Array, int *N)
{
int avg, i;
int sum = 0;
for (i=0; i<*N; i++)
sum = sum + Array[i];
avg = sum / *N;
return avg;
}

## Slide 21: Local Variables
Memory storage for these variables is created on entry into the subroutine and released on exit from subroutine.
The system stack is the ideal place to create memory space for temporary variables.
This temporary memory space is called the stack frame.
Subroutines often use local variables whose scope and life span exist only during the execution of the subroutine.
CE/CZ 1007
Data Structure
(Function)

## Slide 22: Stack Frame
SP
System stack
Stack frame of N words is created on the system stack immediately on entry into a subroutine.
Memory space within the stack frame can be accessed using with a frame pointer (FP) or the stack pointer (SP).
Stack on entry into subroutine
SP
Stack on entry into subroutine
SP
Stack after stack frame allocation
int avg
int i
int sum
int Mean()
{
int avg, i;
int sum = 0;
:
FP
function Mean
Stack frame of N=3 words created for three word-sized local variables in functions Mean.
Frame pointer in ARM can be any register
General convention FP is R11

## Slide 23: Accessing Stack Frame Variables Using the Frame Pointer
Consider the use of a frame pointer register R11.
SP
Original contents of R11 is saved on the stack before it is used as the frame pointer.
Accessing the stack frame
int avg
int i
int sum
Frame Pointer R11
R11-04
R11-08
R11-012
Frame pointer (R11) now points to the saved R11 and a stack frame is created by adding frame size 4N to SP.
Saved R11
R11 is the frame reference and an appropriate negative displacement from R11 can be used to access any stack frame variable.
When exiting the subroutine, the stack frame can be destroyed by adding 4N+4 to SP and copying the saved R11 value on the stack back into R11.

## Slide 24: Accessing Stack Frame Variables Using the Frame Pointer
When exiting the subroutine, the stack frame can be destroyed by adding 4N+4 to SP and copying the saved R11 value on the stack back into R11.
SP
Accessing the stack frame
int avg
int i
int sum
Frame Pointer R11
R11-04
R11-08
R11-012
Saved R11
For N=3
ADD SP, SP, #16
LDR R11,[R11]

## Slide 25: What is the instruction to create a stack frame for 4 local variables (32-bit each)
ADD SP, SP, #5
SUB SP, SP, #4
SUB SP, SP,#16
ADD SP,SP,#16

## Slide 26: If we are using R11 as frame pointer, what is the instruction to store R4 to local variable c
STR R4, [R11,#-1]
STR R4, [R11,#-4]
STR R4, [R11,#-4]!
STMFD R11!,{R4}
int c
Saved R11
int i
int sum

## Slide 27: C Function Example Accessing Parameters & Local Variables
Both parameters passed in and local variables can be accessed using the frame pointer (FP).
SP
int avg
int i
int sum
R3-01
R3-02
R3-03
Saved R3
© W.B.Goh (2013)
int Mean (int *Array, int N)
{
int avg, i;
int sum = 0;
for (i=0; i<N; i++)
sum = sum + Array[i];
avg = sum / N;
return avg;
}
int *Array
Return Address
int N
R3+03
R3+02
The stack
SP
Frame Pointer R3
Parameters pushed on the stack
Call made to subroutine Mean
Frame Pointer (R3) saved and setup
Parameters passed in are accessed using positive offsets from the FP.
Create stack frame for local variables
The stack after setting up local variables
Local variables are accessed using negative offsets from the FP.
Give the instruction to implement this C statement:
movs [R3-1], #0

## Slide 28: Accessing Stack Frame Variables Using the Stack Pointer
A more efficient approach is to use the stack pointer (SP) itself.
SP
Accessing the stack frame
int avg
int i
int sum
Stack Pointer SP
ER6-02
SP+08
SP+04
A stack frame is created by adding frame size 4N to SP.
Appropriate positive displacements from SP is used to access any of the stack frame variables.
Pro - This method is more efficient because there is no need to setup a frame pointer.
Con – More restrictive as system stack cannot be used within subroutine without changing the reference SP.
SP is used as a reference to access all local variables.
Stack Pointer SP
Frame Pointer R11
